## Slide 1
Improving Preparedness of Communities for Evacuations using ZEVs
Definition of use cases for Merced/Mariposa evacuations
Presenter: Qijian Gan (UC Berkeley)
April 26th, 2024

## Slide 2: Problem Statement
Due to the rapid increase of ZEV ownership in recent years, rural areas like in Mariposa are facing a big challenge in the evacuation using ZEVs.
  These rural areas normally lack charging facilities to support mass evacuations using ZEVs.
  The transportation networks are vulnerable to support mass evacuations.
    Very limited routes to nearby cities.
    These routes normally consist of state highways that are 2-lane roadways. Therefore, any traffic incident happening on the roadway will significantly degrade the evacuation effectiveness and efficiency.
    Changes to traffic control at arterial intersections are needed to support the large volume of vehicles traveling in the dominated direction.

## Slide 3: Problem Statement (cont.)
Once the evacuation plans for ZEVs are developed (normally at the planning/macroscopic level), their performance needs to be evaluated at the operational/microscopic level.
  The planning/macroscopic tools may not be able to appropriately capture
    Abnormal traffic congestion at arterial intersections due to the factors like excessive left-turn demands and low intersection throughputs (e.g., at stop signs).
    The impact of traffic incidents, e.g., reduced throughputs, longer travel delays, road blockages, gridlocks, etc.

## Slide 4: Proposed Solution
In this project, we want to develop a microsimulation platform in Aimsun (https://www.aimsun.com/) to support the evaluation of ZEV evacuation plans in the Merced/Mariposa area, which consists of the following:
  A calibrated microsimulation model for the Merced/Mariposa network.
  An enhanced simulation platform with novel features to support
    The modeling and calculation of EV battery consumption in a more dynamic and realistic environment;
    The modeling and management of fixed/mobile charging stations;
    The routing of EVs for charging;
    The modeling and assessment of evacuation plans (e.g., activation/deactivation of new traffic control along the evacuation routes, vehicle routing, performance measures, etc.)

## Slide 5: Current Progress
We have created a microsimulation network in the Merced/Mariposa area.
While creating the network,
  We focused on the scenario of ZEV evacuations from Mariposa to nearby cities (e.g., Merced, Madera, etc.)
  We modeled the major arterials inside Mariposa, the state highways, and other 2-lane roadways.
Mariposa, CA
Planada, CA
Merced, CA
Snelling, CA
Ave 26 (To Chowchilla, CA)
Valley Lake Ranchos, CA
Lake Madera Country Estates, CA
Madera, CA
Rolling Hills, CA

## Slide 6: Current Progress (cont.)
We are in the process of calibrating this microsimulation model.
We need your support if you happen to have or know how to get the following types of data for the study site:
  Travel demand models (for Origin-Destination demands)
  Timing sheets and traffic counts (or the Synchro model) at the signalized intersections
  Traffic counts (or even the AADT) along the state highways and the 2-lane roadways (we might be able to get some data from the PeMS system)
  Other data like probe travel times
AADT: Annual Average Daily Traffic
PeMS: https://pems.dot.ca.gov/
Synchro: https://www.cubic.com/transportation/synchro-studio

## Slide 7: Current Progress (cont.)
Meanwhile, we have finished the architecture design for the modeling of EV charging at fixed/mobile charging stations in Aimsun.
We are currently implementing the required data structures and workflows.
We hope to show this enhanced simulation platform in our next workshop.
AADT: Annual Average Daily Traffic
PeMS: https://pems.dot.ca.gov/
Synchro: https://www.cubic.com/transportation/synchro-studio

## Slide 8: Q&A?